## Slide 1
Touch ON–OFF Sensor Switch
A simple bistable switching circuit using the NE555 timer IC
ECE Mini Project
TOUCH ON
TOUCH OFF
NE555

## Slide 2
1. Introduction
What is a touch ON–OFF sensor switch?
Purpose
Turns a load ON or OFF using a light touch instead of a mechanical switch.
Main IC
The NE555 is configured as a bistable (flip-flop-like) circuit.
Output
The 555 output changes state and can control indicator LEDs or another suitable load.
Two touch plates act as the ON and OFF inputs.
A brief touch changes the state; the circuit remains in that state until the opposite touch is made.
This makes the circuit useful as an electronic replacement for a simple push-button switch.
2

## Slide 3
2. Components Required
Typical parts used in the shown circuit
NE555 timer IC
Main bistable control element
2 touch plates
ON and OFF sensing inputs
Resistors
Provide bias/current-limiting functions
LED1 & LED2
Indicate the output state
DC supply
Powers the NE555 circuit
3

## Slide 4
3. Circuit Diagram
Reference circuit provided for the touch ON–OFF switch
Touch ON
Touch the ON/trigger plate to make the 555 output go HIGH.
Touch OFF
Touch the OFF/reset plate to make the output go LOW.
LED indication
Opposite LED states visually show whether the output is HIGH or LOW.
4
+VCC
GND
NE555
BISTABLE
2 TRIGGER
SET
6 THRESHOLD
RESET
7 DISCHARGE
8 VCC
4 RESET
3 OUTPUT
1 GND
5 CONTROL
NC
TOUCH ON
10kΩ
TOUCH
TOUCH OFF
10kΩ
TOUCH
OUTPUT INDICATION
LED ON
330Ω
330Ω
LED OFF
Pin 7 discharge path
Touch ON → SET → OUT HIGH | Touch OFF → RESET → OUT LOW

## Slide 5
4. Working Principle
NE555 bistable operation in simple steps
1
Initial state
The circuit powers up in one of its two stable output states.
2
Touch ON
A touch changes the trigger-side voltage so the 555 sets its output HIGH.
3
State held
After the touch is removed, the output stays HIGH because the 555 is bistable.
4
Touch OFF
The reset/threshold-side input is activated, causing the output to go LOW.
5
State held
The output remains LOW until the ON touch is made again.
555 thresholds: ≈ 1/3 VCC and ≈ 2/3 VCC
5

## Slide 6
5. ON and OFF Operation
How the LEDs respond to the 555 output
ON state
• Touch the ON sensor. • The 555 output (pin 3) becomes HIGH. • The ON indicator LED lights. • Removing your finger does not immediately change the state; the bistable circuit holds it.
OFF state
• Touch the OFF sensor. • The 555 output (pin 3) becomes LOW. • The opposite indicator LED shows the OFF state. • The circuit remains LOW until the ON sensor is touched again.
6

## Slide 7
6. Advantages and Applications
Advantages
• No moving mechanical switch • Simple and low-cost circuit • Easy ON/OFF control by touch • Output state is latched • Useful for learning timer IC applications
Possible Applications
• Touch-controlled lamps • Small indicator/control panels • Electronic project demonstrations • Educational NE555 experiments • User-interface prototypes For larger loads, use an appropriate transistor, MOSFET or relay driver stage.
7

## Slide 8
7. Conclusion
The touch sensor uses the NE555 as a bistable switching element.
Two touch inputs provide separate ON and OFF control.
The output remains in its selected state after the finger is removed.
LEDs provide a simple visual indication of the output state.
The project demonstrates practical concepts of touch sensing, thresholds and digital switching.
Thank You
8